## Slide 1: 2017 HazCom Refresher
City Of Anderson SC

## Slide 2: OSHA’s Revised HAZCOM Standard (3/26/2012)
Your Right to Know and Understand
Hazardous Chemicals Used in the Workplace
Safety Policies & Programs
GHS
The
Globally Harmonized System
Of Classification and Labeling of Chemicals

## Slide 3
Evolution of the OSHA HAZCOM Standard
1983 – OSHA First Implements its Hazardous Communications Standard for Manufacturing ONLY
1987 – OSHA Expands to Include All Industries
1994 – Changes for Multi-Employer Worksites
2012 – OSHA adopts the International Approach Called the Globally Harmonized System (GHS) of Classification and Labeling of Chemicals (Rev 3)
Rev 4

## Slide 4
OSHA’s Revised HAZCOM standard
Effective Completion Date | Requirement(s) | Who
March 26, 2012 | Final Rule Published | OSHA
December 1, 2013 | Train Employees | Employers
Transition Period | Comply with Old and Begin Compliance with New HCS Standard | All chemical manufacturers, importers, distributors and employers
June 1, 2015 | Compliance) | All chemical manufacturers, importers, distributors and employers
December 1, 2015 | Distributors may ship products labeled under the old system until this date | Distributors
June 1, 2016 | Update workplace labeling and HAZCOM program | Employers

## Slide 5
Changes to the OSHA HAZCOM Standard
Old OSHA HAZCOM Standard:
Material Safety Data Sheets (MSDS) Are Performance Based -Required Content But No Set Format
  Information Was Different For Each Company
  Workers Had Difficulty Understanding Information
  The Length and Complexity Made It Difficult to Locate Important Safety Information
Chemical Product Labels Had Minimal Information

## Slide 6
This Standard Update Gives Workers Access to Labels and Safety Data Sheets with Information that is Easier to Find and Understand as well as the Right to Know
NEW OSHA HAZCOM Standard with GHS:
  Prescribes a 16-Part Safety Data Sheet (SDS) Format and Contents
  Chemical Product Labels Require New Prescribed Information Linked to New Criteria for Health and Physical Hazard Classifications and Categories
Changes to the OSHA HAZCOM Standard

## Slide 7
Changes to the OSHA HAZCOM Standard
Material Safety Data Sheets
The Primary Source for
Chemical Product Hazard Information
Are Now Called
Safety Data Sheets
Must be in English
Should be Available in Languages of ESOL Workers

## Slide 8
Got a Question
  Don’t Know If a New Product Can Cause Illness
  How Do You Use It and Protect Yourself
  What Do You Do In Case of a Spill
SDS Safety
Data
READ the SDS Before You Use the Product
  Lists Routes of Entry, Symptoms of & Care if Exposed
  Recommends PPE, Handling, Storage & Cleanup
The Vendor Should Provide You a SDS With Purchase
  If Not, Ask For SDS
If Product Is Not Listed in BCB’s On-Line Inventory,
the Supervisor Must Send SDS to BCB Safety

## Slide 9
Changes to the OSHA HAZCOM Standard
Safety Data Sheets – 16 Part Format:
  Section 1: Identification – Includes the
    Product Identifier
    Manufacturer ‘s or Distributor’s
      Name
      Address
      Phone Number
      Emergency Phone Number
    Recommended Use
    Restrictions on Use

## Slide 10
Changes to the OSHA HAZCOM Standard
Safety Data Sheets – 16 Part Format:
  Section 2: Hazard(s)Identification
    All Hazards Regarding the Chemical
    Required Label Elements
  Section 3: Composition / Ingredients
    Information on Chemical Ingredients
    Trade Secret Claims

## Slide 11
Changes to the OSHA HAZCOM Standard
Safety Data Sheets – 16 Part Format:
  Section 4: 1st Aid Measures
    Important Symptoms and Effects
      Acute or Delayed
    Required Treatment
  Section 5: Fire-Fighting Measures
    Lists Suitable Extinguishing Techniques and Equipment
    Chemical Hazards From Fire

## Slide 12
Changes to the OSHA HAZCOM Standard
Safety Data Sheets – 16 Part Format:
  Section 6: Accidental Release Measures
    Emergency Procedures
    Protective Equipment
    Proper Containment and Cleanup
  Section 7: Handling and Storage
    Precautions for Safe Handling and Incompatibilities

## Slide 13
Changes to the OSHA HAZCOM Standard
Safety Data Sheets – 16 Part Format:
  Section 8: Exposure Controls / Personal Protection
    Permissible Exposure Limits
    Threshold Limit Values
    Engineering Controls
    Personal Protective Equipment
  Section 9: Physical & Chemical Properties
    Chemical’s Characteristics

## Slide 14
Changes to the OSHA HAZCOM Standard
Safety Data Sheets – 16 Part Format:
  Section 10: Stability & Reactivity
    Lists Possibility of Hazardous Reactions
  Section 11: Toxicological Information
    Routes of Exposure
    Related Symptoms
    Acute and Chronic Effects
    Numerical Measures of Toxicity

## Slide 15
Changes to the OSHA HAZCOM Standard
Safety Data Sheets – 16 Part Format:
  Section 12: Ecological Information
  Section 13: Disposal Considerations
  Section 14: Transport Considerations
  Section 15: Regulatory Considerations
  Section 16: Other Information
    Date of Preparation or Last Revision
Enforced by Other Agencies (Not OSHA)

## Slide 16
Changes to the OSHA HAZCOM Standard
LABELS – as of Dec 1, 2015
will be required to have:
Product Identifier
Signal Word
Hazard Statement
Pictograms
Precautionary Statement
Supplier Identification
ToxiFlam (Contains: X Y Z)
Danger!
Toxic If Swallowed
Flammable Liquid and Vapor
Do not eat, drink or use tobacco when using this product. Wash hands thoroughly after handling. Keep container tightly closed. Keep away from heat/sparks/open flame – No Smoking. Wear protective gloves and eye/face protection. Ground container and receiving equipment. Use explosion-proof electrical equipment. Take precautionary measures against static discharge. Use only non-sparking tools. Store in cool/well ventilated place.
IF SWALLOWED: Immediately call a POISON CONTROL CENTER or doctor/physician. Rinse mouth.
In case of fire, use water fog, dry chemical, CO2 or “alcohol” foam.
See Safety Data Sheet for further details regarding this product.
MyCompany, MyStreet, MyTown NJ 00000
Tel: 444 999 9999
SAMPLE

## Slide 17
Changes to the OSHA HAZCOM Standard
ToxiFlam (Contains: X Y Z)
Danger!
Toxic If Swallowed
Flammable Liquid and Vapor
Do not eat, drink or use tobacco when using this product. Wash hands thoroughly after handling. Keep container tightly closed. Keep away from heat/sparks/open flame – No Smoking. Wear protective gloves and eye/face protection. Ground container and receiving equipment. Use explosion-proof electrical equipment. Take precautionary measures against static discharge. Use only non-sparking tools. Store in cool/well ventilated place.
IF SWALLOWED: Immediately call a POISON CONTROL CENTER or doctor/physician. Rinse mouth.
In case of fire, use water fog, dry chemical, CO2 or “alcohol” foam.
See Safety Data Sheet for further details regarding this product.
MyCompany, MyStreet, MyTown NJ 00000
Tel: 444 999 9999
LABEL:
Product Identifier - the
Chemical Name
Product Name or
Other Unique Identifier
  Used On Both
  the Label
  and the
  Safety Data Sheet
SAMPLE

## Slide 18
Changes to the OSHA HAZCOM Standard
ToxiFlam (Contains: X Y Z)
Danger!
Toxic If Swallowed
Flammable Liquid and Vapor
Do not eat, drink or use tobacco when using this product. Wash hands thoroughly after handling. Keep container tightly closed. Keep away from heat/sparks/open flame – No Smoking. Wear protective gloves and eye/face protection. Ground container and receiving equipment. Use explosion-proof electrical equipment. Take precautionary measures against static discharge. Use only non-sparking tools. Store in cool/well ventilated place.
IF SWALLOWED: Immediately call a POISON CONTROL CENTER or doctor/physician. Rinse mouth.
In case of fire, use water fog, dry chemical, CO2 or “alcohol” foam.
See Safety Data Sheet for further details regarding this product.
MyCompany, MyStreet, MyTown NJ 00000
Tel: 444 999 9999
LABEL:
Signal Word
Indicates the Severity of the Chemical Hazard
  DANGER – Most Severe
  Warning – Less Severe
SAMPLE

## Slide 19
Changes to the OSHA HAZCOM Standard
ToxiFlam (Contains: X Y Z)
Danger!
Toxic If Swallowed
Flammable Liquid and Vapor
Do not eat, drink or use tobacco when using this product. Wash hands thoroughly after handling. Keep container tightly closed. Keep away from heat/sparks/open flame – No Smoking. Wear protective gloves and eye/face protection. Ground container and receiving equipment. Use explosion-proof electrical equipment. Take precautionary measures against static discharge. Use only non-sparking tools. Store in cool/well ventilated place.
IF SWALLOWED: Immediately call a POISON CONTROL CENTER or doctor/physician. Rinse mouth.
In case of fire, use water fog, dry chemical, CO2 or “alcohol” foam.
See Safety Data Sheet for further details regarding this product.
MyCompany, MyStreet, MyTown NJ 00000
Tel: 444 999 9999
LABEL:
Hazard Statement
  Describes the Nature and Degree of the Chemical Hazard
  Standardized Phrase is Pre-Determined by its Chemical Classification and Category
    As Evaluated by the Manufacturer In Accordance With OSHA Criteria
SAMPLE

## Slide 20
Changes to the OSHA HAZCOM Standard
ToxiFlam (Contains: X Y Z)
Danger!
Toxic If Swallowed
Flammable Liquid and Vapor
Do not eat, drink or use tobacco when using this product. Wash hands thoroughly after handling. Keep container tightly closed. Keep away from heat/sparks/open flame – No Smoking. Wear protective gloves and eye/face protection. Ground container and receiving equipment. Use explosion-proof electrical equipment. Take precautionary measures against static discharge. Use only non-sparking tools. Store in cool/well ventilated place.
IF SWALLOWED: Immediately call a POISON CONTROL CENTER or doctor/physician. Rinse mouth.
In case of fire, use water fog, dry chemical, CO2 or “alcohol” foam.
See Safety Data Sheet for further details regarding this product.
MyCompany, MyStreet, MyTown NJ 00000
Tel: 444 999 9999
LABEL: Pictograms
  a Black Symbol (Determined By the Chemical’s Classification & Category )
  on a White Background
  with a Red Border
  Conveys Specific Information About the Hazards of the Chemical
SAMPLE

## Slide 21
Changes to the OSHA HAZCOM Standard
LABEL: Pictograms
Oxidizer – Material May Cause Ignition of Combustibles Without External Source of Ignition
Flammables, Self-Reactives, Pyrophorics, Self-Heating, Emits Flammable Gas, Organic Peroxides
Flame Over Circle
Flame
Explosives, Self-Reactives, Organic Peroxides
Exploding Bomb

## Slide 22
Changes to the OSHA HAZCOM Standard
LABEL: Pictograms
Corrosives – Chemical Action Eats or Wears Away Thus Weakening or Destroying Metals, or Burns Skin or Eyes
Corrosion
Acute Toxicity (Severe) – Poisonous; Capable of Causing Serious Debilitation or Death
Skull and Crossbones
Gases Under Pressure
Gas Cylinder

## Slide 23
Changes to the OSHA HAZCOM Standard
LABEL: Pictograms
Carcinogen; Respiratory Sensitizer; Mutagenicity;
Or Reproductive, Target Organ or Aspiration Toxicity
Health Hazard
Irritant, Dermal Sensitizer, Acute Toxicity (harmful), Narcotic Effects, Respiratory Tract Irritant
Also Voluntarily Identifies Substances Hazardous to the Ozone
Exclamation Mark

## Slide 24
Changes to the OSHA HAZCOM Standard
LABEL: Other Pictograms You May See
Biological Substances Can Be Hazardous But Are Not Regulated by OSHA
Biological
Acute or Chronic Aquatic Toxicity
Enforced By EPA (Not OSHA)
Environment
Exempt:
Consumer Products
Articles That Under Normal Conditions Pose No Physical Hazard or Health Risk
  Can Change If Cut Into or Welded

## Slide 25
Changes to the OSHA HAZCOM Standard
ToxiFlam (Contains: X Y Z)
Danger!
Toxic If Swallowed
Flammable Liquid and Vapor
Do not eat, drink or use tobacco when using this product. Wash hands thoroughly after handling. Keep container tightly closed. Keep away from heat/sparks/open flame – No Smoking. Wear protective gloves and eye/face protection. Ground container and receiving equipment. Use explosion-proof electrical equipment. Take precautionary measures against static discharge. Use only non-sparking tools. Store in cool/well ventilated place.
IF SWALLOWED: Immediately call a POISON CONTROL CENTER or doctor/physician. Rinse mouth.
In case of fire, use water fog, dry chemical, CO2 or “alcohol” foam.
See Safety Data Sheet for further details regarding this product.
MyCompany, MyStreet, MyTown NJ 00000
Tel: 444 999 9999
LABEL:
Precautionary Statements
Describes Recommended Measures to Minimize or Prevent Adverse Effects Resulting From Exposure or From Improper Handling or Storage
Standardized Phrases are Pre-Determined by its Chemical Classification and Category
SAMPLE

## Slide 26
Changes to the OSHA HAZCOM Standard
ToxiFlam (Contains: X Y Z)
Danger!
Toxic If Swallowed
Flammable Liquid and Vapor
Do not eat, drink or use tobacco when using this product. Wash hands thoroughly after handling. Keep container tightly closed. Keep away from heat/sparks/open flame – No Smoking. Wear protective gloves and eye/face protection. Ground container and receiving equipment. Use explosion-proof electrical equipment. Take precautionary measures against static discharge. Use only non-sparking tools. Store in cool/well ventilated place.
IF SWALLOWED: Immediately call a POISON CONTROL CENTER or doctor/physician. Rinse mouth.
In case of fire, use water fog, dry chemical, CO2 or “alcohol” foam.
See Safety Data Sheet for further details regarding this product.
MyCompany, MyStreet, MyTown NJ 00000
Tel: 444 999 9999
LABEL:
Supplier Identification
  The Name
  Address and
  Telephone Number
  Of the
  Chemical Manufacturer
  Importer or
  Other Responsible Party
SAMPLE

## Slide 27
LABELs:
Do Not Open / Use
the Container If:
  No Label
  Torn or Partially Missing Label
  Label You Cannot Read
the OSHA HAZCOM Standard
Report to Supervisor
or BCB Safety for Replacement or Disposal

## Slide 28
LABELs Not Required On:
Portable Containers -
When Transferred For Personal Use (by that Employee) ONLY
Must Be Used by End of Shift
Must Have Label If Passed On to Another Worker
Piping Systems
the OSHA HAZCOM Standard

## Slide 29
OSHA’s Revised HAZCOM Standard
New Labels with Added Information
  Signal Word
  Hazard Statement
  Pictograms
  Precautionary Statement
New Safety Data Sheet Format with 16 Prescribed Parts
How to Find SDS on SiteHawk: BCB’s On-Line Inventory
QUESTIONS???
Safety Policies & Programs
Contact BCB Safety: Holly Bockow, 737-2311 / Bernie Lee, 737-2315